## Slide 1: Patriot Jr.™
Equipment Overview

## Slide 2
Overview of the machine’s capabilities and components
General instructions for operation, shutdown, maintenance, and prevention

## Slide 3: Basic Functions
Able to dispense 2-part urethane low-rise adhesive
Accommodates 5-Gal Jugs/BIB and 15-Gal Drums
Intended to increase production compared to Dual Cartridge, Dual Tanks, and PaceCart

## Slide 4
Customized cart holds Flexible FAST™ 5-Gal Jugs and 15-Gal Drums without additional attachments or conversion kits
PJR cart is designed to carry Graco pump, a DeWalt air compressor, and a 3000w generator without the need for additional carts on the roof
Includes a lockable compartment to store additional parts
Handle and wheel design makes cart easy to maneuver
Built-in forklift slots make transporting and loading the cart even easier

## Slide 5: Fittings
Each PJR comes with a set of reusable fittings to accommodate both packaging options – 5-Gal Jugs or 15-Gal Drums
The design for male/female fittings are mirrored for Part A and Part B to help avoid crossover

## Slide 6: Graco Pump
Utilizes an OEM GRACO Reactor
Stays mounted on the PJR cart

## Slide 7: PJR Hoses
These are your primary hoses that move material from pump to gun
PJR Hose Bundle
These are secondary hoses used to help prevent damage to primary hoses
Whip Hose

## Slide 8: Gun Options
Gun Options | Bead Application | Splatter Application | Air Purge Feature
Vee Manifold | X |  | 
Vee Air | X | X | X

## Slide 9: PJR Setup

## Slide 10: Brand New PJR Setup
  If not already installed, mount the PJR Reactor onto the PJR Cart. MAKE SURE ALL CLIPS AND HOLD DOWNS ARE SECURE.
1
  Connect fluid hoses to the pump and the gun. Ensure hoses are connected properly according to the PJR directions and videos.
2

## Slide 11: Brand New PJR Setup
  If using the Vee-Air gun, mount the air compressor onto the bottom rack of the PJR cart. MAKE SURE ALL CLIPS AND HOLD DOWNS ARE SECURE.
3

## Slide 12: Flexible FAST Drum Setup

## Slide 13: Flexible FAST Drum Setup
  Ensure the storage compartment located on the backside (or drum side) of the PJR is closed and in a locked position.
1

## Slide 14: Material Temperature
Material temperature for Flexible FAST adhesive must be at least 70°F for proper application to occur.
25°F (2°C)
40°F (4°C)
45°F (7°C)
50°F (10°C)
55°F (13°C)
60°F (16°C)
65°F (18°C)
70°F (21°C)
75°F (24°C)
80°F (27°C)
85°F (29°C)
90°F (32°C)
95°F (35°C)
100°F (38°C)
Optimum Chemical Temperature at Time of Application
(Process core chemical temperature)
Temperature Range
Maximum Storage Temperature
Minimum Storage Temperature
Minimum Surface Temperature

## Slide 15: Flexible FAST Drum Setup
  With the help of another person, carefully stand the PJR Cart in an upright position. DO NOT ATTEMPT WITH ONLY ONE PERSON.
2

## Slide 16: Flexible FAST Drum Setup
  Carefully open the Flexible FAST drums and connect the PJR fittings. USE WHITE LITHIUM GREASE AT EVERY CONNECTION BEFORE FITTINGS ARE INSTALLED.
3
  The large bung fitting connects to the desiccant dryer.
  The small bung fitting connects the drum to the machine.

## Slide 17: Flexible FAST Drum Setup
  Using the color-coded labels located on the backside (or drum side) of the PJR, place each drum in a vertical position next to the PJR cart. Ensure each drum corresponds with the proper
  A- and B-side.
4

## Slide 18: Flexible FAST Drum Setup
  Once all fittings have been installed and are absent of air/fluid leaks, you may then carefully place the drums onto the drum rack while it is in its vertical position.
5
  NOTE: Once the A- and B-sides have been designated, DO NOT CROSS-CONTAMINATE WITH OPPOSITE CHEMICAL AT ANY TIME.

## Slide 19: Flexible FAST Drum Setup
  Secure drums firmly to the cart using the provided ratchet straps. Make sure drum straps are in the locked position before proceeding to the next step.
6

## Slide 20: Flexible FAST Drum Setup
  Connect corresponding cam lock fitting to A and B drums and ensure vent pipes remain capped.
7
  DOUBLE CHECK ALL FITTINGS AND CLIPS to ensure everything is secure and tightened.
  DOUBLE CHECK FLUID VALVES to ensure they are in the closed position.

## Slide 21: Flexible FAST Drum Setup
  With the help of another person, pull the PJR Cart down from the upright position.
8
  Pull the PJR Cart all the way down so that the drums are parallel to the deck. Ensure both the wheels and rear legs are firmly on the deck.

## Slide 22: Changing Drums

## Slide 23: Switching out Flexible FAST Drums
Ensure Flexible FAST Drums are strapped to the cart and the storage compartment is closed and in a locked position.
2
Ensure all fluid valves are closed and machine has been properly powered down.
1
With the help of another person, carefully stand the PJR cart in an upright position. DO NOT ATTEMPT with only one person.
3
Remove ratchet straps from the drums.
4
Remove the PJR fittings from the used drums and install bung caps into the bung holes.
5
To install new drums onto the PJR cart, refer to steps 4-8 from Flexible FAST Drum Setup.
6

## Slide 24: Startup and Dispensing

## Slide 25: Daily Startup and Dispensing Procedures
  Apply a small amount of pump lube to each piston on the A- and B-side pumps.
1

## Slide 26: Daily Startup and Dispensing Procedures
  If using a generator, place the generator in the tray between the drums. Ensure it is properly fueled and oiled.
2
  Plug the PJR cord into your power source.
  DO NOT USE IDLE CONTROL if using a generator.
3

## Slide 27: Daily Startup and Dispensing Procedures
  Remove the tape on the top and bottom sides of each desiccant drier. Install a desiccant drier into the vent fittings on each drum.
4

## Slide 28: Daily Startup and Dispensing Procedures
  Before turning on the PJR machine, ensure that both recirculation valves are completely closed.
5

## Slide 29: Daily Startup and Dispensing Procedures
  Completely open both fluid valves leading from the drums.
6
  You should see A- and B-side materials fill up the clear tubing prior to the next step.
Fluid Valve (closed position)

## Slide 30: Daily Startup and Dispensing Procedures
  Turn the orange power switch to “on”.
7
  Without a mixing tip, open valves on the gun and set the flow dial to 1 or 2. This will start pulling material throughout the pump, hose, and gun.
8

## Slide 31
Check for two equal streams of A- and B- chemical to visibly flow from the gun.
9
  Once fluids are flowing evenly with no air pockets, close the fluid valves on the gun and turn the safety to “on”. Apply white lithium grease to the threads on a NEW static mixing tip and install mixing tip on the gun.
10
Daily Startup and Dispensing Procedures

## Slide 32: Bead Application
  When beads or ribbons are specified at 4”, 6”, or 12” on-center.
11

## Slide 33: Daily Startup and Dispensing Procedures
  With gun valves closed, turn the flow dial to 3-5.
a

## Slide 34
  Release the safety and open fluid valves on the gun to begin applying adhesive.
b
  Ensure the adhesive is dispensed at a minimum ½”- ¾” wet bead and proper spacing is followed.
c
Daily Startup and Dispensing Procedures

## Slide 35
Wet Bead
Foam Bead with String Time

## Slide 36: Splatter Application
  The following equipment and settings listed MUST be followed for approved splatter application.
12

## Slide 37: Daily Startup and Dispensing Procedures
  PJR Flow Dial Setting: 6
a

## Slide 38
  Air compressor pressure: 80psi
b
  Air setting on gun: 1/8 turn or 0.5 setting.
  Open ONE valve only.
c
  Fluid valves on gun: 100% open
d
NOTE: Pressure may need to be adjusted depending on the temperature of the material.
Daily Startup and Dispensing Procedures

## Slide 39
Initial Splatter
Splatter with String Time

## Slide 40
When you have reached a stopping point, ensure the gun is pointed in a safe direction and close any open fluid or air valves on the gun.
13
  Once valves are closed, discard the static mixing tip and replace with a new one.
14
Daily Startup and Dispensing Procedures

## Slide 41: Short-Term Shutdown

## Slide 42: Short-Term Shutdown Checklist (overnight/lunch break)
  Ensure you have reached a proper stopping point and the gun valves are closed.
1
  Turn down the fluid dial to its “off” position, turn off the power switch, and unplug the power cord on the PJR.
2

## Slide 43
  Apply a new static mixing tip and apply white lithium grease through the grease fittings on the gun. Fill mixing tip with about 2”-3” of grease.
3
Short-Term Shutdown Checklist (overnight/lunch break)

## Slide 44
  Close both fluid valves leading from the drums to the pump.
4
  Remove desiccant driers from the drums. Apply tape to the top of each drier and cover with a plastic bag as needed.
5
  Add caps back on the vent tube top. Remember to use white lithium grease on all fittings.
6
Short-Term Shutdown Checklist (overnight/lunch break)

## Slide 45: Short-Term Shutdown Checklist (overnight/lunch break)
Apply a small amount of pump lube to each piston.
7
  Wrap up hose and gun and protect all equipment with the provided green PJR cover. Secure as needed.
8

## Slide 46: Long-Term Shutdown

## Slide 47: Long-Term Shutdown Checklist (2 weeks or longer)
Close both fluid valves leading from the drums to the pump.
2
Ensure the gun valves are closed and the machine has been shut down properly.
1
Remove desiccant driers from the drums. Apply tape to the top of each drier and cover with a plastic bag as needed.
3
Add caps and plugs back on the vent tube top. Remember to use white lithium grease on all fittings.
4
With the help of another person, carefully stand the PJR Cart in an upright position. DO NOT ATTEMPT with only one person.
5

## Slide 48: Long-Term Shutdown Checklist (2 weeks or longer)
  Disconnect inlet hoses from the drums. Ensure fittings on the drums have been properly plugged/capped.
6
Side A
Side B

## Slide 49
  Using the open end of the additional set of connect hoses provided, connect the appropriate A- and B-side inlet cam locks.
7
Long-Term Shutdown Checklist (2 weeks or longer)

## Slide 50
  Place A-side hose in a container of ISO Flush.
8
  Place B-side hose into a container of ISO Flush.
9
Long-Term Shutdown Checklist (2 weeks or longer)

## Slide 51
  Using an empty trash receptacle, open both fluid valves from the drums and both fluid valves on the gun.
10
  Turn on power and set flow dial to “circulate” and allow flush to run through pump, hose, and gun until clear fluid is observed.
11
Long-Term Shutdown Checklist (2 weeks or longer)

## Slide 52: Long-Term Shutdown Checklist (2 weeks or longer)
Turn fluid dial to “off”.
13
Once clear fluid is observed, close fluid valves on the gun AND from the drums.
12
Pull the flush hoses from the ISO Flush containers and insert hoses into new containers of Surf-A-Lube.
14
Using a trash receptacle, open both fluid valves from the drums and both fluid valves on the gun.
15
Turn flow dial to “circulate” and allow lube to run through pump, hose, and gun until clear lube is present.
16

## Slide 53
  Once clear lube is observed, close fluid valves on the gun and from the drums.
17
  Turn the fluid dial to its “off” position, turn off the power switch, and unplug the power cord on the PJR.
18
Long-Term Shutdown Checklist (2 weeks or longer)

## Slide 54
  Apply a new static mixing tip and apply grease through the grease fittings on the gun. Fill mixing tip with about 2”-3” of grease.
19
  Disconnect additional connector hoses and install plugs/caps on cam locks.
20
Long-Term Shutdown Checklist (2 weeks or longer)

## Slide 55
  Wrap up hose and gun and protect all equipment with the provided green PJR cover. Secure as needed.
21
Long-Term Shutdown Checklist (2 weeks or longer)

## Slide 56: Prevention and Troubleshooting

## Slide 57: Prevention
Apply pump lube before and after each use to both pistons.
2
Use white lithium grease for all fittings, securements, plugs/caps, and mixing tips. This helps prevent material buildup and seals all possible passages for air and moisture.
1
Letter-label or color-code fittings, desiccant driers, plugs/caps, and containers. This helps ensure that fittings and accessories stay on their designated A- or B-side.
3
Ensure all openings have been plugged unless being vented properly.
*Replace desiccant driers when needed.
4
Blue = good
Pink = needs replaced
When in doubt, flush it out. Flushing your machine regularly and often will significantly increase the operating life of your PJR and reduce downtime on the jobsite.
5

## Slide 58: Troubleshooting Tips
Ensure both passages in the gun are clear by using a 1/4" drill bit.
2
Proper storage of material is essential. Ensure the material temperature of Flexible FAST is 70°F at all times.
1
Ensure both check valves from the drums are open completely.
3
Ensure both ends of the desiccant driers are completely open.
4
Ensure the Y-screens are clear and free of debris or crystals. Replace if needed.
5
Ensure all fittings are completely secure and tightened with no air leaks.
7
Ensure hose assemblies from the drums are clear of debris or crystals. Replace if needed.
6
Ensure hoses are free of all kinks and twists.
8
Ensure a new static mixing tip is being used after stopping for 30 seconds or longer.
9

## Slide 59: Adhesive Cost Savings with the Patriot Jr.

## Slide 63: Questions?